## Slide 1: RRWCD meeting
RRCA Accounting
April 25, 2019

## Slide 2: RRCA
RRCA – Republican River Compact Administration
  Three States (Kansas, Nebraska, Colorado)
  Unanimous vote required for action
  Non-Compliance not an option
RRCA annual Accounting
  Computed Beneficial Consumptive Use (CBCU) by each state (a.k.a stream impacts)
    Includes SW and GW uses

## Slide 3: RRCA Accounting
Accounting is completed annually
  First data share is April for previous years use. Each state provides data to the modeler including pumping data, diversion data, etc. i.e. we are providing 2018 data in April 2019.
  The modeler acquires climate data from NOAA after it is released (final sometime in spring)
  NASS data is acquired (late June) to confirm crop information.
  Model runs in late July –early August for final accounting.
  Final accounting approval late August at RRCA annual meeting

## Slide 4: RRCA Accounting
Accounting process memorialized in the 2002 Final Settlement Stipulation (FSS) Appendix C -88 pages) approved by the US Supreme Court
Accounting manual approved by the RRCA
Accounting requires certain data:
  Surface water diversions
  Groundwater calculated depletions to streams
Accounting compares each states CBCU with the states consumable allocation.

## Slide 5: RRCA Accounting
Accounting inputs are:
  Irrigation use (GW and SW)
  Non-irrigation uses (think municipal, etc)
  Reservoir evaporation
  Streamflow at selected gages
Accounting efficiencies are:
  Surface irrigation CBCUs is 60% of diversion
  Surface water non-irrigation CBCUs is 50% of diversion.
  Groundwater irrigation efficiency is 83% of diversion (CBCUg is determined for the whole state by a GW model).
  Groundwater M&I efficiency is 50% of diversion (CBCUg determined by Model as above)

## Slide 6: RRCA Accounting
RRCA accounting does not include:
  Irrigation of less than 2 acres
  Non-irrigation diversion of less than 50 acre-feet/year
  Non-federal reservoir evaporation from reservoirs that hold less than 15 acre-feet/year.
  Uses outside of the RRCA groundwater model domain

## Slide 7: RRCA Accounting – Surface Water
Surface water irrigation CBCUs is 60% of the diversion.
  Example: 1000 af diversion = 600 af CBCUs in accounting.
Surface water reservoir CBCUs is 100% of the evaporation
  Example: Reservoir evaporates 3500 af. CBCUs is 3500 af.

## Slide 8: RRCA Accounting – Groundwater “The Computed Beneficial Consumptive Use of groundwater for each State shall be determined as the difference in streamflows using two runs of the model”
Groundwater impacts (CBCUg) are not observable so a model is used to calculate the CBCUg the stream would see.
Model inputs include: pumping, crop data, climate data, irrigated acreage, etc.
The model takes into account the total amount of net pumping from the aquifer, the resulting changes in storage in the aquifer, and then the resulting depletion to the stream summed up at specific compact locations.
The model is a regional model covering parts of 3 states and is not designed to determine the effect of a single well or small group of wells.
The model is operated on a state on/state off basis where one state is turned off while the other states are on…this allows for the accounting to not double-count impacts caused by the three states. The difference between these runs are used to determine the CBCUg at the end of each basin.

## Slide 9: RRCA Accounting - Groundwater
Based on the total pumping for each state a summary of the CBCUg for each basin for each state is an output from the model.
That table goes into the accounting.
Impacts 2017 (acre-feet) |  |  |  | 
Location | Colorado | Kansas | Nebraska | Nebraska
 | Pumping | Pumping | Pumping | Mound
Arikaree | 2102 | 157 | 77 | 0
Beaver | 0 | 6391 | 4451 | 0
Buffalo | 502 | 0 | 3544 | 0
Driftwood | 0 | 0 | 891 | 0
Frenchman | 1206 | 0 | 75001 | 0
North Fork | 16906 | 0 | 1174 | 0
Above Swanson | -3304 | 101 | 6821 | 0
Swanson - Harlan | -26 | -198 | 30673 | 8493
Harlan - Guide Rock | 0 | 0 | 26220 | 492
Guide Rock - Hardy | 0 | 53 | 2546 | -12
Medicine | 0 | 0 | 20362 | 10337
Prairie Dog | 0 | 6979 | 0 | 0
Red Willow | 0 | 0 | 6155 | 37
Rock | 112 | 0 | 5064 | 0
Sappa | 0 | 2305 | 2183 | 62
South Fork | 12225 | 4621 | 699 | 0
Hugh Butler | 0 | 0 | 2092 | 0
Bonny | 1312 | 16 | 0 | 0
Keith Sebelius | 0 | 572 | 0 | 0
Enders | 12 | 0 | 4917 | 0
Harlan | 0 | 71 | 746 | 30
Harry Strunk | 0 | 0 | 333 | 0
Swanson | 14 | 0 | 272 | 0
Mainstem | -3330 | -36 | 66260 | 8973
Total | 31063 | 21082 | 194223 | 19454
MS's 4 reaches + 2 reservoirs | (3,316) | 27 | 67,278 | 9,003
Above Guide Rock | (3,316) | (26) | 64,732 | 9,015
Total of individual sub-basins | 31,061 | 21,068 | 194,221 | 19,439
Total - GR to Hardy | 31,063 | 21,029 | 191,677 | 19,466

## Slide 10: RRCA Accounting
The accounting takes the GM output and the surface water diversions and, using the formulas in the FSS and procedures in the RRCA accounting manual, determines the status of each states compliance.
For the long term average (1995-2017) pumping in Colorado of 727,000 af, the average CBCUg was 27,400 af (or 3.7%)